## Slide 1
RadialMamba: Coordinate-Augmented Swin-UMamba for IV-OCT Segmentation
INPUT AND COORDINATE CHANNELS
SWIN-UMAMBA BACKBONE
Internal SS2D scan operators unchanged
OUTPUT
IV-OCT input
Preprocess
and crop
512 × 512
RGB patch
Primary A/B training
Dice–Focal + foreground sampling (0.5)
Encoder
Decoder
Encoder
stage
Encoder
stage
Encoder
stage
Encoder
stage
Decoder
stage
Decoder
stage
Decoder
stage
Decoder
stage
Skip connections
Segmentation
head
Deep supervision
Main loss weight: 4/7
Aux
head
Dice + Focal
2/7
Aux
head
Dice + Focal
1/7
Aux
head
Weight = 0
Four-class segmentation
Prediction
Ground truth
Illustrative development case
Lumen
Fibrous cap
Lipid core
Vasa vasorum
Feature flow
Skip connection
Auxiliary supervision
Schematic encoder–decoder organization
Patch-local coordinates
Cy
Cx
Notes: RadialMamba augments RGB patches with local x, y, r channels and uses the existing Swin-UMamba backbone for multiclass segmentation. The figure summarizes the encoder–decoder organization, skip connections and auxiliary Dice–Focal supervision. The internal SS2D scan operators remain unchanged. The coordinate channels refer to the current input patch rather than a catheter-centered anatomical reference. The primary matched comparison shares loss and sampling settings between the coordinate and RGB-only arms. Class weighting and VV-specific sampling belong to the separate joint refinement, not the primary recipe illustrated here. The clinical overlays are retained illustrative examples from the earlier development experiments, not new hold-out results. Source: author-provided Schema.pptx and the revision experiment handoff. The RGB/Cx/Cy/Cr artwork and concatenation bracket follow the author-provided original illustration. Cx, Cy and Cr each contribute one coordinate channel, giving six channels together with RGB. The illustrated radial map refers to the center of the current patch. The layered planes are a conceptual channel illustration. Homepage export: x denotes height and y denotes width. Deep-supervision weights are 4/7, 2/7, 1/7, 0. The medical images are an illustrative development case from the author-provided source figure, not results from the revised holdout evaluation.